## Slide 1: Flash Gas Estimation
Thomas Manuel Ortiz, Ph.D., P.E.
June 11, 2019

## Slide 2
Tankless Oil Gathering Systems Will Soon Be Common
Lease Boundary
High Vapor Pressure Oil
Calculated Flash Gas
Calculated Stable Oil
Measured Gas
Measured Water

## Slide 3
Process Simulation Models Will Replace Some Meters
Process simulation software can predict the separation of oil and gas using thermodynamic models called Equations of State (EOS)

## Slide 4
Verifying EOS: Flash Liberation Testing in the Lab
Reservoir Pressure and Temperature
Separator Pressure and Temperature
Oil
Oil
Gas
Hg
Hg
Removing mercury from the test cell allows the pressure to drop and gas to evolve from the oil

## Slide 5
The Importance of a Controlled Laboratory Environment
Flashing a liquid from high to low pressure will release a large amount of stored energy.
Image Source: [1]

## Slide 6
Oil
Oil
Gas
Hg
Hg
Oil
Gas
Hg
T1, P1
T2, P2
T3, P3
Oil Continues to “Shrink” When Flashed Repeatedly
>
>

## Slide 7
Oil
Gas
Gas
T2, P2
T3, P3
And Flash Gas Composition Changes Every Time
>
C1
C2
C3
C4
C5
C6+
Flashes First
Flashes Last
Lighter Hydrocarbons
Leaner Gas
Lower Heating Value
Heavier Hydrocarbons
Richer Gas
Higher Heating Value

## Slide 8
Heater Treater
Heavier Gas
Oil Shrinkage
We Can See This By Reading Lab Reports

## Slide 9
Reference Separation Stage by Specific Gravity

## Slide 10
Flash Gas Calculation Using Gas Oil Ratio (GOR)
for every 1000 STB of stock tank oil through a two-stage separator train having the GOR values shown
Stage 1 Flash Gas
GOR = 148 Scf/STB
Stage 2 Flash Gas
GOR = 45 Scf/STB
A well produces
1000 x (0.148 + 0.045)
= 193 Mscf
of flash gas (i.e. a total GOR = 193 SCF/STB)
“Produced Gas”
Not Included Here. Includes free, or “casinghead” gas

## Slide 11
Flash Gas Energy Attributable to These Volumes

## Slide 12
GLO Engineering Has Developed A New Flash Tool
Relies on the Peng-Robinson Equation of State to perform flash calculations.
Can be used to independently estimate flash gas
Preferable to Vasquez-Beggs for high API gravity (40+) oils [2]

## Slide 13
STB
The tool underpredicts flash gas by 5%, which is to be expected since multiple stages will increase the amount of flash gas. Multistage tool (in development) will result in more accurate calculations.
Flash Results Using New Tool

## Slide 14
Comparison to Vasquez-Beggs (V&B) Correlation
Caveat: Actual 3 Phase Separator gas gravity not provided in report.
Is it OK to estimate gas gravity from RRC Form G-5 data for this well?

## Slide 15
Model Inputs Must Always Be Mutually Consistent
No, it isn’t appropriate to use a gas gravity that was generated at 404 psia in a model that is being run at 289.65 psia (275 psig)

## Slide 16
But We Can Run Sensitivity Analyses
Chart: Gas Gravity
| 0.6 | 0.65 | 0.7 | 0.75 | 0.8
GOR | 134.703 | 145.928 | 157.153 | 168.378 | 179.604
To obtain a GOR of 193 SCF/STB using V&B, we would have to input a gas gravity of 0.86. Is that a reasonable value of gravity for our conditions?

## Slide 17
Power Function Fit of Pressure vs Gas Gravity
This is a purely mathematical, rather than a physical, model, but it does give us an indication of the trend.

## Slide 18
V&B Likely Underpredicts GOR
Gas gravity ranges from 0.55 for very lean gases to 1.5 for very rich gases, with a “typical” value being 0.65. [3]
It is possible, though unlikely, that the initial, 3 Phase Separator gas at 275 psig was rich enough to have a gravity > 0.85.
This leads us to conclude that V&B likely underpredicts the GOR in this case, but we don’t know by how much unless we can obtain the true gas gravity.
Again, these results are from a single-stage model, which means that underprediction of flash gas is to be expected vis a vis two-stage separation

## Slide 19
But, Wait! We Found The True Gas Gravity After All!
And it is quite close to the value predicted by our power function fit.

## Slide 20
Recomparison to Vasquez-Beggs (V&B) Correlation
So, in conclusion, V&B underpredicts flash gas by 13% in this case. Recall that the new GLO flash calculation tool underpredicted flash gas by only 5%.

## Slide 21
Initial Version of Flash Tool Available Now on O: Drive

## Slide 22
Try It Yourself Using Sample Data
Can you match the Volumes using the GLO tool? How close is “close enough”

## Slide 23
Model Calibration Can Be Difficult
EOS models often must be calibrated, or “tuned” to the particular crude oil being flashed
Extensive tuning typically means that physical sample quality is poor
“PVT experiment” data is required for tuning
  For instance, the differential liberation test data shown here
GLO Engineering will work with you to establish guidelines for reasonable uncertainty bounds

## Slide 24
Future Work
Support up to four separation (flash) stages
Connect flash to Processed Gas tab
  Automatically generate processed gas values
Create command line mode
  Automatically run multiple inputs as batch job
Automate script data input from database
  Check lease reporting values every month
  Requires data submission from lessees

## Slide 25
Questions?

## Slide 26
GLO Energy Resources relies on a library of spreadsheets for sharing engineering calculations with the Minerals Audit team
If the engineer and auditor aren’t talking about exactly the same calculations, then mistakes can occur.
GLO Energy Resources engineers have ported the spreadsheet library to Python, whereupon engineering calculations will be maintained on and served from the GLO network with Excel-based output.
Single, verified source of calculations
Secure, transparent updates
Includes process simulation workflows
GLO Energy Engineering Calculation Engine Project
xlwings
DWSIM

## Slide 27
References
Desktop Computer, https://en.wikipedia.org/wiki/Desktop_computer
Champagne Opening, https://all-free-download.com/free-photos/download/champagne-opening-moments_165737.html
Texas Commission on Environmental Quality (2012), “Calculating Volatile Organic Compounds (VOC) Flash Emissions from Crude Oil and Condensate Tanks at Oil and Gas Production Sites”, Air Permit Reference Guide APDG 5942, https://www.tceq.texas.gov/assets/public/permitting/air/Guidance/NewSourceReview/guidance_flashemission.pdf , p. 15
Fekete Associates, “Gas Gravity”, http://fekete.com/SAN/TheoryAndEquations/WellTestTheoryEquations/Gas_Gravity.htm